Crystal Structure Report for B. Cossairt

by Sarah Flowers & Werner Kaminsky

Sample Submitted by Dylan Gary

ID – dg_03

X-ray Crystallography Laboratory

University of Washington

05. August 2015

Data backup accessibly through http:

URL: http://cad4.cpac.washington.edu/structures

Data Collection  started:  July 24,2015

Documentation finished: August 4, 2015

W.Kaminsky: tel. (206) 543 7585

(x-ray lab):     tel. (206) 543 0210

Email: kaminsky@chem.washington.edu

Understanding crystallographic information is not trivial. If you discuss a structure in a publication, please let the crystallographers proof-read the final draft of that manuscript before you submit it.

For many structures it is true that crystallography is an intellectual performance (like synthesis or elucidation of mechanisms) and not a routine job. In these cases, particularly when the structures contribute significantly to the content of the publication, the crystallographers should be co-authors. Do not think this is not necessary because you pay for structures. Even I  have to pay for my own structures for my research.

A yellow piece, measuring 0.30 x 0.19 x 0.18 mm3 was mounted on a loop with oil.  Data was collected at -173oC on a Bruker APEX II single crystal X-ray diffractometer, Mo-radiation.

Crystal-to-detector distance was 60 mm and exposure time was 60 seconds per frame for all sets.  The scan width was 0.5o.   Data collection was 99.5 % complete to 25o  in (.  A total of  382918 reflections were collected covering the indices, h = -29 to 29, k = -30 to 30,  l = -51 to 51.  84779 reflections were symmetry independent and the Rint = 0.0785 indicated that the data was of average quality.  Indexing and unit cell refinement indicated a triclinic lattice.  The space group was found to be P(1 (No. 2).

The data was integrated and scaled using SAINT, SADABS within the APEX2 software package by Bruker.

Solution by direct methods (SHELXS, SIR97) produced a complete heavy atom phasing model consistent with the proposed structure. The structure was completed by difference Fourier synthesis with SHELXL97., Scattering factors are from Waasmair and Kirfel. Hydrogen atoms were placed in geometrically idealised positions and constrained to ride on their parent atoms with C---H distances in the range 0.95-1.00 Angstrom. Isotropic thermal parameters Ueq were fixed such that they were 1.2Ueq of their parent atom Ueq for CH's and 1.5Ueq of their parent atom Ueq in case of methyl groups. All non-hydrogen atoms were refined anisotropically by full-matrix least-squares.

Solvent analysis discovered two distinct voids filled with ethyl acetate and related contribution to the diffraction pattern was removed with SQEEZE

With this size of the molecule comes the possibility of disorder, which may have contributed to larger than expected positive as well as negative rest electron densities around the indium atoms, estimated to about 5%. Some disorder of the phenyls was treated explicitly as some inter molecular ‘squeezing’ occurs. As a result of the large molecular size (11.7 kD) and strong scattering of the In-P-cluster, carbon atoms were weekly represented in the data, requiring DELU (In-O-C) and ISOR (O, C) restraints. In addition, the general geometry of the organic ligands was linked via SAME commands.

The structure is of high quality and ready for publication. Table 1 summarizes the data collection details. Figure 1 shows an ORTEP of the asymmetric unit.

Figure 1. ORTEP of the structure with thermal ellipsoids at the 25% probability level. Disorder omitted for clarity.

Table 1: Crystallographic data for the structures provided.

Empirical formula 	C408 H357 In37 O102 P20

Formula weight 	11759.65

Temperature 	100(2) K

Wavelength 	0.71073 Å

Crystal system 	Triclinic

Space group 	P -1

Unit cell dimensions	a = 24.2059(13) Å	= 94.394(3)°.

b = 25.0500(11) Å	= 91.966(3)°.

c = 42.7930(19) Å	 = 115.651(2)°.

Volume	23256(2) Å3

Z	2

Density (calculated)	1.679 Mg/m3

Absorption coefficient	1.933 mm-1

F(000)	11468

Crystal size	0.300 x 0.190 x 0.180 mm3

Theta range for data collection	1.383 to 25.350°.

Index ranges	-29<=h<=29, -30<=k<=30, -51<=l<=51

Reflections collected	382918

Independent reflections	84779 [R(int) = 0.0785]

Completeness to theta = 25.000°	99.5 %

Absorption correction	Semi-empirical from equivalents

Max. and min. transmission	0.722 and 0.595

Refinement method	Full-matrix least-squares on F2

Data / restraints / parameters	84779 / 58044 / 5798

Goodness-of-fit on F2	1.133

Final R indices [I>2sigma(I)]	R1 = 0.1109, wR2 = 0.2992

R indices (all data)	R1 = 0.1790, wR2 = 0.3499

Largest diff. peak and hole	4.011 and -1.679 e.Å-3

# Endnotes

Bruker (2007) APEX2 (Version 2.1-4), SAINT (version 7.34A), SADABS (version 2007/4), BrukerAXS Inc, Madison, Wisconsin, USA.

(a) Altomare A, Burla C, Camalli M, Cascarano G L, Giacovazzo C, Guagliardi A,   Moliterni AGG, Polidori G, Spagna R. (1999) SIR97: a new tool for crystal structure determination and refinement Journal of Applied Crystallography, 32, 115-119.

(b) Altomare A, Cascarano G L, Giacovazzo C, Guagliardi A. (1993) Completion and refinement of crystal structures with SIR 92. Journal of Applied Crystallography, 26, 343-350.

Sheldrick GM. (1997) SHELXL-97, Program for the Refinement of Crystal Structures. University of Göttingen, Germany.

Mackay, S.; Edwards, C.; Henderson, A.; Gilmore, C.; Stewart, N.; Shankland, K.; Donald, A. (1997) MaXus: a computer program for the solution and refinement of crystal structures from diffraction data. University of Glasgow, Scotland,.

Waasmaier, D.; Kirfel, A. (1995) New Analytical Scattering Factor Functions for Free Atoms and Ions. Acta Crystallographica A., 51, 416-430.

A. Spek, J. Appl. Cryst. (2003), 36, 7-13; P. van der Sluis & A. L. Spek, Acta Cryst. (1990). A46, 194-201.

Farrugia LJ. (1997) Ortep-3 for Windows. Journal of Applied Crystallography, 30, 565